GPS Disciplined NTP
Presentation by Wyatt Zacharias
2021
Except where otherwise noted this work is licensed under the Creative Commons Attribution-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-sa/4.0/.

---
Introduction
GPS Time
- The US GPS system is made up of a constellation of satellites in orbit to provide seamless coverage of the entire globe.
- Currently 31 satellites are in orbit with a minimum of 24 required for operation.
- By comparing the time based signals sent from each satellite a GPS receiver can triangulate its position on the earth.
- In order to accomplish this location calculation, the GPS receiver must synchronize its internal clock with the received GPS signals.

---
Image Public Domain, United States Government
Image Copyright, Lockheed Martin

---
GPS Receivers
- All GPS receivers must be able to accurately synchronize their internal clock in order to function, but not all chipsets make this available externally.
- PPS – Pulse per second is a function where the chipset will modulate an output pin at 1Hz synchronized to its internal clock.
- More advanced receivers can be configured to output at different frequencies above or below 1Hz
- Receivers typically interface via RS-232/UART. USB receivers are most often simple serial converters.

---
Image CC-BY-SA 4.0, by Raimond Spekking
Image Copyright, Uputronics
Image Copyright, ublox

---
Chipset Communication
- Several “Standards” have been established to define the communication protocols used by GPS chipsets.
- NMEA-0183 defines a standard set of ASCII messages that a receiver will output, and a standard format for sending control messages to the receiver.
- SiRF defines their own binary message and command format which is widely used and supported due to the prevalence of devices.
- Manufacturers provide full command references for modern chipsets.

---
GPS Signal Reception
- GPS satellites orbit at approximately 20,000KM above earth with a meager transmitter power of only 25W
- Received signal strength on earth is approximately -128dBm in ideal conditions.
- Nearly all receivers employ an active antenna which contains an internal amplifier to increase the level of received signal.
- At 1575Mhz cable loss is significant and must be accounted for when pairing a receiver with an antenna.

---
Link Budget Copyright, FCC

---
MAX-8 Specifications Copyright, ublox

---
RaspberryPi I/O
- The Rpi’s GPIO pins make it an excellent candidate for interfacing with a GPS chipset.
- UART serial used for receiving location data from the chipset and sending commands.
- i2c used to communicate with the internal RTC in the chipset
- Pulse per second sends logic high to selected GPIO pin

---
Time Pulse Graph Copyright, ublox

---
GPSd
- Many implementation guides for GPS time include the use of GPSd to read the time signals from the receiver.
- Serial devices are typically exclusive access which limits you to a single consumer on the system.
- GPSd provides a standard socket interface that provides time and location data in JSON format.
- By distributing the data with GPSd multiple services can consume the location data simultaneously.
- To achieve accurate distribution of PPS data, GPSd uses shared memory segments.

---
NTP Configuration
- NTP has built in support for many types of reference clocks, including GPS & PPS.
- PPS alone cannot provide the current time to NTP.
- For NTP to function fully there must be a second source of “full time” in addition to the PPS signal.
- Secondary time can be provided by GPS, or even another NTP server.
- The secondary time source does not need to be precisely accurate as long as it stays within the PPS timing.

---
Limitations
- Antenna unknowns
- Receiver unknowns
- OS Jitter
- Network Jitter
- Temperature changes
- User error